## Slide 1
Fast I/O Library for Icestick
Midpoint Presentation
Benjamin Braun & Nate Chizgi
Notes: 1

## Slide 2
Implement a library in magma for icestick FPGA ↔ CPU I/O…
  Currently, communicating between the CPU and a running icestick is hard!
… that makes common communication patterns easy:
  Visual Data: graphics rendered on FPGA displayed on CPU screen in real-time
  Debugging / Log Data: printf() “statements” in magma show in CPU terminal
  Stream Data: file on CPU read to FPGA program, output written back to file.
Disclosure: we hope to have a demo for one, possibly two, of these patterns
Goals
Notes: 2

## Slide 3
Few choices for an I/O primitive to unmodified Icestick
  UART is the only primitive that doesn’t require hardware mod
  … but it’s slow and unreliable
Complex semantics of different communication patterns
  What should the library look like?
Challenges
Notes: 3

## Slide 4
Demo UART runs at 115,200 baud
  ~7 KBps
  Visual data cap: 64x64 1 FPS @ 8-bits/pixel
We found the FTDI chip will support up to 12,000,000 baud
  Results in 0.715 MBps streaming FPGA→CPU
  Visual data cap: 640x480 2 FPS @ 8-bits/pixel
I/O Primitive
UART is slow
Notes: 4

## Slide 5
Problem: FPGA→CPU data dropped if buffers on FTDI chip overflow
  As far as we know, they are silently dropped without notifying CPU
Solution: Add backpressure mechanism
  Require CPU to signal “ACK” of received data to FPGA
  FPGA will wait to send more data unless earlier data was ACKed
  Effectively limits the amount of in-flight data FPGA→CPU at any time
I/O Primitive
UART is unreliable
Notes: 5

## Slide 6
I/O Primitive
Reliable UART
Reliable UART
(fast version)
IF= # in-flight
Notes: 6

## Slide 7
Implementing Communication Patterns
Magma code
requiring visual display
FPGA layout
Fast-IO circuitry
Generated binary
(with GUI)
Communication
Compiles to...
Notes: 7

## Slide 8
Implementing Communication Patterns
Magma code
with “printfs”
FPGA layout
Fast-IO circuitry
Generated binary
(outputs to stdout)
Communication
Compiles to...
Notes: 8

## Slide 9
Magma code
using Fast-IO library
“.iospec” file (produced as side-effect)
Verilog
Compiles to... (magma)
+
Compiles to... (icestorm)
Compiles to... (our own “iocc” script)
FPGA layout
C++ program
Compiles to... (our own “iocc” script)
C++ program
Compiles to... (gcc)
Generated Binary
Notes: 9

## Slide 10
//”Hello world” for procedural graphics using Icestick Fast-IO
magma.main()
conn = ifio_connection(UART) //use UART (only option for now)
display = ifio_simpledisplay(conn, 640, 480, 60) //width, height, framerate
def my_procedural_graphics():
return AnonCircuit(
in16 X,
in16 Y,
in32 frameCount,
//dynamic black-and-white diagonal gradient
Out32 out = X + Y + FrameCount
)
gfx = my_procedural_graphics()
gfx(display.X,display.Y,display.FrameCount)
wire(gfx.out, display.pixelOut)
magma.compile()
Icestick Fast-IO Library API
Notes: 10

## Slide 11
ifio_connection(...)
  Define connection properties. Pass result as argument to below:
ifio_simpledisplay(width,height,framerate,details)
  make a width x height display @ framerate, other args in “details”
ifio_display()
  “Advanced” version of simpledisplay (details omitted)
ifio_printf(formaSame as simpledisplay except t_string,arg_description)
  Prints data to CPU stdout on any clock cycle where “enable” line is 1
ifio_stream_process(“file_in.txt”,”file_out.txt”)
  Exposes data from “file_in.txt” to FPGA whenever FPGA sets “ready”
  Exposes FPGA output to “file_out.txt” whenever FPGA sets “valid”
+ more communication patterns?
Icestick Fast-IO Library API
Notes: 11

## Slide 12
Few choices for an I/O primitive to unmodified Icestick
  Fast reliable UART
  Library abstracts away I/O primitive
Complex semantics of different communication patterns
  Library API is specialized for a set of common patterns
  Easy to use, at the expense of some flexibility
Challenges Addressed
Notes: 12

## Slide 13
Thank you!

## Slide 14
Backup Slides

## Slide 15
IOSpec(<type>, paramList)
  Support various simple streaming types with user defined transforms/callbacks
Types
  DisplayInOut(x_res, y_res, fps, fd…)
  DisplayOut(x_res, y_res, fps, fd)
  Printf(numPort)
  ReadLines(userCB, numPort, fd)
  WriteLines(userCB, fd)
Icestick Fast-IO Library API
Fast-IO API
Notes: 15

## Slide 16
For demonstration purposes, implementing overclocked UART RX/TX
  UART support is built in to Icestick device without any device level modifications –
  Other (parallel/faster) protocols available through device level soldering
Able to achieve 0.715 MBps with overclocked UART (12MHz baud)
  Good for 640x480 2 FPS 8-bit / pixel
  Other future enhancements discussed in ‘future work’ to improve throughput
Streaming Protocol
Design Decisions - Modified UART
Notes: 16

## Slide 17
Printf flow chart
Example compilation flow
CPU side program
  Hold bulk of message
  Flatten pre-processed args
  Arg count & bitwidth
FPGA side program
  Control header
    msg idx (tie w/CPU)
    Length
    Drop ind. (conflict)
  Argument body
    Concatenated body
  Print at some event
Notes: 17

## Slide 18
Display Rendered Stream (Time-varying gradient video)
  Output pixel brightness = f(x,y,time) = x+baud(t)
  Display = DisplayOut(x_res=640, y_res=480, fps=60, playback)
  userCirc = userRenderGradient(display.x, display.y, baud)
Output time-stamped debug trace to bin file (waveform viewer)
  Output concat(data, timestamp) from several (5) usr defined modules
  userCB = counter(timestamp_res, baud)
  Write = writeLines(userCB, numPort, binary)
  UserModA(dbgOut=Write.port[0]) … UserModZ(dbgOut=Write.port[N])
Output print statements from several User modules
  Printf = printf(numPort)
  UserModA(dbgOut=printf.port[0]) … UserModZ(dbgOut=printf.port[N])
Streaming Examples
Simplified support for common use cases
Notes: 18